## Slide 1
Tag Attachment Methods

## Slide 2
Gluing tags to birds – Holberton & Tudor
© D. Hamilton
© R. Holberton

## Slide 3
1: trim small patch of fur between scapulae using trimming scissors (disinfect)
2: Apply thin coat of surgical glue (SkinBond) to tag.
3: Apply thin layer of glue to exposed patch of skin and wrap surrounding hair over tag, allowing antenna to trail straight behind bat.
4: hold for about ~5 minutes to ensure glue sets and tag attaches.
5: disinfect all tools/materials used according to WNS decontamination guidelines before handling another bat.
Gluing tags to bats – Peterson

## Slide 4
Materials:
Elastic 1mm thread, like for bracelet making, and loctite super glue
Sizing:
published dimensions for leg loops (Naef-Daenzer 2007)
trial– record mass/size for good fits
Have a few sizes available each day
Deploying
http://www.holohil.com/rappole.htm
Check that the feet are perching, wings are free, up over very top of leg- reassess
Leg Loop harnesses - Smetzer
(Rappole and Tipton 1991)
Longer tag retention
  MINIMAL glue- tag can come off eventually
Recaps did not exhibit abrasion or injury
4mm
4mm
4mm
35mm

## Slide 5
Suture and Glue Tag Attachment for Terns
P. Paton
Pam Loring – UMass Amherst

## Slide 6
Materials
Ethicon Prolene
  Size 4-0, taper point, 3/8 circle, 30"
  Expired (non-sterile) less expensive
Q-tips and isopropyl alcohol
Needle drivers (2), scissors (1) – ask for donations
Adhesive (Loctite 422, Loctite Gel Epoxy 6 min dry time, others?)
Sharps container
For the bird: pillow, head cone, person to hold

## Slide 7
Process
Rest bird on pillow, head in cone
Minimize talking to reduce bird stress & movement
Little blood supply between feather tracks
Apply alcohol with Q-tip to part feathers and check position
Use fingers to tent skin and needle drivers to insert sutures (top and bottom)
Tie off with surgeons knot & 3 square knots. Tension on 1st throw most important. Make sure knots lie flat (not twisted).
Apply glue to underside of tag and to each knot and hold still until dry

## Slide 8
Custom Attachment Tubes
2013
2014

## Slide 9
Acknowledgements
Linda Welch (Maine Coastal Islands NWR)
Rob Ronconi (Acadia University)
Mark Pokras, DVM (Tufts University)
Lynn Miller (Cape Wildlife Center)
Kate Iaquinto (Monomoy NWR)
Norm Smith (Mass Audubon)
Carolyn Mostello (MA Natural Heritage Program)
Mike Vandentillaart (Lotek Wireless)
P. Paton

## Slide 10
Power Minimizing Strategies with PV

## Slide 11
Holberton
To PV